## Slide 1: Automated Green House Humber College: ELIC 606 By: Shawn G. A. Bullock http://members.fortunecity.com/tproject

## Slide 2: Project Overview
The aim of this project was to:-
Design a system that will completely automate a greenhouse.
The system uses the C++ programming language to develop software that monitors the temperature and soil moisture data from a hardware system within the greenhouse and perform task such as watering and cooling automatically. Thus eliminating the need for human labour.
The data collected is stored in a spreadsheet file and presented graphically through LABVIEW.
The entire software system is to be presented as a stand-alone test system with security features that can be installed on any standard Intel 80486 or higher system running Windows 95 of higher.

## Slide 3: Design Elements
The development of this system was done by creating three sub-systems that uniformly work together.
1) First a hardware system had to be developed to measure temperature and soil moisture information and condition their signals so they were compatible with IBM PC parallel port standards.
2) Second a software program had to be developed to control the hardware, acquire data from the hardware and store the acquired data in a format that labview could read and analysis.
3) Finally a software program with LABVIEW for data analysis and security had to be developed.
Next each subsystem will be described.

## Slide 4: Hardware: Temperature
Signal conditioned a 3Kohm thermistor for an output voltage range of 0-3.85V which represents 10 C -40C.
Thermistor has a non-linear output as shown below and characterized by the equation.
Ro(T) = Ro (To)[eY(T-1-To-1)]
Where:
Ro(T) is the resistance at Temperature T
Ro (To) is the resistance at 25C (3K)
E is 2.718
Y is 2923.94 + 4.8657T – 0.005363T2
T is the temperature at which R is unknown
expressed in degrees Kelvin (273.15 + C)
To is 298.15 degrees Kelvin
Too complicated for time allotted.
Decided to use small temperature (10 C – 40 C) range and a relatively accurate yet linear relation as shown in figure.

## Slide 5
The slope of the 10C and 30C resistances was used to signal condition this thermistor because this line is fairly accurate for this range
The accuracy starts to be loss around above and below this range. According to the data sheet the resistance at 40C is 1.598K but with the applied linear relationship it would be represented by 0.917K.

## Slide 6
Signal Conditioning
To generate a voltage change that was proportional to the 10C to 40C temperature change, the thermistor was placed as one element of a wheat stone bridge (powered with a 5VDC).
The differential voltage produced across Va and Vb represented the change in temperature. The other three elements of the wheat stone bridge were 3, 10KΏ potentiometers set to exactly 6KΏ resistors because the resistance at 10C (minimum temperature) is 5.97KΏ +/- 10%
To determine the differential voltage of this bridge at 40C the thermistor was replaced with 0.920KΏ of resistors (resistance at 40C). The differential voltage at this point was found to be 1.837V.
Therefore the differential voltage range for a temperature range of 10c – 40c is 0V – 1.837V.
This was verifier mathematically as shown below.
Va = 5V x (6KΏ/12KΏ) = 2.5V
Vb = 5V x (0.917KΏ/6.917KΏ) = 0.663V
Therefore, Va – Vb = 1.837V

## Slide 7
The 0V - 1.84V output of the wheat stone bridge had to be amplified for input to the ADC.
To do this a TLC271 single source opamp was used with a source voltage of 0-5V.
Configured as a differential amplifier. The signal was amplified to 3.85V (gain of about 2.2) because that is the max output for the TLC272 single source opamp used when Vdd is 5V.
Gain = 2.2 = 22Kohm/10Kohm

## Slide 8: Soil Moisture
Used a simple bi-metallic probe that displays the moisture level of soil on a standard galvanometer.
It operates as a simple battery.
The potential difference across the two metallic elements is proportional to the soil moisture level.
Since no data specification sheets were available for this device I had to measure the potential difference across the two leads at different moisture levels and determine its characteristics. Moisture Level
Moisture Level Voltage (mV)
0 0
2 55
4 112
6 168
8 225
10 280
Results showed that the moisture level is change is linear at a rate of 28mV per moisture level.

## Slide 9
Since the probe generates it’s own voltage a differential amplifier was used to amplify the 280mV (level 10) output by a gain of 13.75 to 3.85V.
The signal was amplified to 3.85V because that is the max output for the TLC272 single source opamp used when Vdd is 5V.

## Slide 10: Analog to Digital conversion for PC parallel port I/O
Used ADC0804 8-bit ADC because of its high resolution.
IBM PC Parallel port only inputs 4 bits at a time. To get around this problem a 2-to1 (8 inputs to 4 outputs) multiplexer 74LS157 was connected to the ADC outputs. This allowed the computer to take in the date 4 bits at a time. Software was used to reconstruct this data back into its original 8-bit byte.

## Slide 11: Fan, Heater, Water Sprinkler
Two 12V, 120mA computer fan were used.
A red fan was used rather then a heater because I was unable to find one.
The output from the parallel port is 5V 26mA, which is not enough to power the fans.
To get around this problem BJT transistor switching circuits were used
Ra = Vcc/Ic-sat = 12V/120mA = 100ohms
Ic-sat = 12V/100ohms = 120mA
Ib-sat = Ic-sat/B = 120mA/100 = 1.2mA
Ib-on = 10X1.2mA = 12mA
Therefore, Rb = 5V/12mA = 417ohms ≈ 470ohms
WATER SYSTEM
- An LED was used to show the output to turn on water since a pump was to expensive.

## Slide 12: C++ Software
To best explain the software I will explain the flow of the program now and you will be able to further understand how it works during the demonstration at the end of this presentation.

## Slide 13
Starts with an Introduction screen
Waits for operator to hit any key before it continues, thus allowing time to turn on the hardware.
--------------------------
Request user input the sample rate in minutes.
Starts sampling when user presses enter.

## Slide 14
Create Binary file.
Displays error message and continues if file can not be created d
Checks if keyboard input received
If no key hit continue, else go to step 16
Inputs temperature data
Inputs soil moisture data
Calculates average temperature of all temperature samples to date and time since start of sampling
Convert inputted temp and soil values from 8-bit hex value to a temp between 10 –40 degrees and a level between 0 and 10
Display temperature, soil moisture level, sample number, time since first sample, and average of all temperatures collected on the screen.
Check if temp is greater then 35 degrees and if so outputs hi signal to bit 3 of port 0x378 to turn on fan.
Check if temp is less then 15 degrees and if so outputs hi signal to bit 7 of port 0x378 to turn on heater.
12. Check if soil moisture is less then level 3 and if so outputs hi signal to bit 3 of port 0x278 to turn on water system
13. Writes sample number, time since first sample, average temperature, current temperature, and current moisture level to the open file.
14. Run delay equal to sample rate minus program execution time
15. Go to step 3
16. Close file
17. Exit to windows

## Slide 15: Collecting the ADC data
unsigned char getADCData(void) {
outport(data_port1,0x00); // Bit 0 of the data port outputs low signal to ADC write line
delay(100); // 100 msec. delay to compensate for hardware delay
outport(data_port1,0x01); // Bit 0 of the data port outputs high signal to ADC write line
delay(100); // 100 msec. delay to compensate for hardware delay
outport(control_port1,0x00); // Bit 2 of control port outputs low signal to multiplexer chip select line
delay(100); // 100 msec. delay to compensate for hardware delay
low1 =inport(status_port1); // Inputs lower 4 bits of ADC output
low1=(low1 >>3); // Shift bits into correct bit locations
low1=(low1 & 0x0f); // Mask the upper 4 bits.
outport(control_port1,0x04); // Bit 2 of control port outputs high signal to multiplex chip select line
delay(100); // 100 msec. delay to compensate for hardware delay
high1=inport(status_port1); // Inputs upper 4 bits of ADC output
high1=(high1 <<1); // Shift data into correct bit locations
high1=(high1 & 0xf0); // Mask the lower 4 bits.
data=(high1 + low1); // Addi the two shifted and masked numbers inputted
return data; // Return value of this function

## Slide 16: Labview Interface
The labview interface is a software application that
allows the user to login in to the system, run the C++
program, and display the temp and soil data on graphs.

## Slide 17
This program basically requires that the user login in with a password before the C++ program or anything else can be run.
Once a valid username and password is entered the remainder of the program can be run.
After the C++ program is closed the user can see the temperature or soil data on a bar graph by hitting the button to do so.
When the user is ready to close the program he or she can do so by hitting the stop button to close the program and return to windows.

## Slide 18: Login Verify VI
The while loop continually runs until the name entered is the same as one in column 0 of the table. The false case runs till the name matches.
Once the name matches the true case starts and the password entered is compared with the password of the matched name.
The equal function is used to check if the name input matches a table entry and if the password also matches the table entry.
The less then function controls the while loop conditional. The loop continues to run while the current iteration number is less than the number of rows in the table. The NOR function also controls the while loops conditional so that the loop continues until a match is found.
The select function is used along with the password matching. If the password matches the current name is sent to the name confirmed indicator. Otherwise, the empty string is sent.

## Slide 19: Start C++ program VI
This VI uses the system execute function to run the C++ program when the start program button is hit.

## Slide 20: Temperature Data and Soil Data VI’s
The Read Spreadsheet function read the data from the disk file created.
The Index Array functions read the values from each column of the file and rewriting it into two rows of a 2-D array. Column 0 contained the sample number and column 2 contained the temperature at the time of sampling.
The 2-D array’s contains was then outputted to a Spreadsheet Table function.
This VI also sends the temperature values sampled to a waveform graph that displays temperature versus sample number.
The soil VI is the same except column 4 was index not 2.

## Slide 21: Exit Labview to Windows
When the stop button is presses a false state is sent to the while loop conditional so the application stops running. The quit labview function is used to cause the application to completely close labview and return to the operating system.

## Slide 22: Other Things:- -ISA PPI Interface -Web Page ----------------------------- DEMONSTRATION